## Slide 1: Prediction of alcohol consumption
Team:Beginners
manoj
meghana
kavitha
sruthi

## Slide 2: REQUIREMENTS:
HARDWARE:
NODEMCU
MQ3 SENSOR
BASIC SHIELD
BUZZER
SOFTWARE:
IBM WATSON CLOUD PLATFORM
MIT APP INVENTOR

## Slide 3: Features of MQ-3 Alcohol Sensor:
Sensor Type - Semiconductor
Easy SIP header interface
Compatible with most of the microcontrollers
Low-power standby mode
Requires heater voltage
Good sensitivity to alcohol gas
Fast response and High sensitivity
Long life and low cost
Requires simple Drive circuit

## Slide 4: Pin Description For MQ-3 Sensor Module
Pin Name
VCC
GND
Digital Out (DO)
Analog Out (AO)
Description
This pin powers the module, typically the operating voltage is +5V
Used to connect the module to system ground
You can also use this sensor to get digital output from this pin, by setting a threshold value
This pin outputs 0-5V analog voltage based on the intensity of the gas using the potentiometer

## Slide 5: Specifications of MQ-3 Gas Sensor:
Power requirements: 5 VDC @ ~165 mA (heater on) / ~60 mA (heater off)
Current Consumption: 150mA
DO output: TTL digital 0 and 1 ( 0.1 and 5V)
AO output: 0.1- 0.3 V (relative to pollution), the maximum concentration of a voltage of about 4V
Detecting Concentration: 0.05-10mg/L Alcohol
Interface: 1 TTL compatible input (HSW), 1 TTL compatible output (ALR)
Heater consumption: less than 750mW
Operating temperature: 14 to 122 °F (-10 to 50°C)
Load resistance: 200kO
Sensitivity S: Rs(in air)/Rs(0.4mg/L Alcohol)=5
Sensing Resistance Rs: 2K?-20K?(in 0.4mg/l alcohol)
Dimensions: 32 x 22 x 16 mm

## Slide 6: Applications of MQ-3 Gas Sensor:
Gas level over-limit alarm
Breathalyser
Portable alcohol detector
Stand-alone/background sensing device
Environmental monitoring equipment